## Slide 1: Security Hardening of Industrial Control Systems through Attribute Based Access Control
Shwetha Gowdanakatte, Mahmoud Abdelgawad, and Indrakshi Ray
Ninth Annual Industrial Control System Security (ICSS) Workshop
October 2023
Austin, Texas, USA
Department of Computer Science

## Slide 2: Outline
Introduction
Background
    PLC and their Security Vulnerabilities
    NIST NGAC for PLC
Attack demonstration
    Attack Model
    DoS Attack on the PLC
Security Hardening
    ABAC Gateway
    Testbed
    Prevention of DoS Attack with ABAC Gateway
Formal Verification
    Use Case 1: PLC without ABAC Gateway
    Use Case 2: PLC with ABAC Gateway
Formal Analysis
Conclusion & Future work

## Slide 3: Industrial Control Systems (ICS)
Human Machine Interface (HMI)
Programmable Logic Controller (PLC)
Remote Monitoring and Control (RMC)
Actuators
Sensors
Controlled Process
set points, parameter, control algorithms, constraints, process data
manipulated variable
controlled variables
process outputs

## Slide 4: Background: PLC and their Security Vulnerabilities
Programmable Logic Controllers
  Rockwell Compact Logix
    Engineering Framework: Studio 5000
    Communication Protocol: Common Industrial Protocol (CIP)
Recent Vulnerabilities
  CVE-2021-1392: Obtain a CIP password and add an authorized admin user
  CVE-2021-22681: Bypass authentication to impersonate Studio 5000
  CVE-2016-9342: Crafted TCP packets to the PLC

## Slide 5: Background: NIST NGAC for PLC
Attribute-Based Access Control for PLC: Gowdanakatte et al. [1]
[1] Shwetha Gowdanakatte, Indrakshi Ray, and Siv Hilde Houmb. 2022. Attribute Based Access Control Model for Protecting Programmable Logic Controllers. In Proceedings of the ACM Workshop on Secure and Trustworthy Cyber-Physical Systems (CODASPY). ACM, Baltimore, MD, USA, 47–56.

## Slide 6: Background: Policy Formalization
Each policy is expressed as a tuple
<{User Attribute}, {Resource Attribute},{Environmental Attribute},{operation}>
User Attributes
  Access Level = {Operator, Engineer, Administrator}
  Device ID
Resource (PLC) Attributes
  Module = {Software, Firmware, Communication, Memory}
  Status= {Stopped, Running, Emergency Stop Active}
  Operating Mode = {Program, Test, Error, Remote}
  Port
Environmental Attributes
  User Access Time
  User Access Location
Example Policy: Communication Setup
  <{(User.AccessLevel ∈ {Operator, Engineer, Administrator), (User.Device = “Equip 21L OrgABC”)},
  {(PLC.OperatingMode = Remote)}, {(Env. Access Time = 700 − 16 : 00EST),
  (Env. Access Loc = OrgABC.local”)}, {CommSetup}>

## Slide 7: Attack Model
Phase-1: Man-in-the-Middle (MITM) Attack
Engineering Workstation
PLC
Attacker
Establish communication
Process communication
Intercept and capture packets
Extract firmware version
Create Crafted TCP packets

## Slide 8: Attack Model
Phase-2: Denial of Service (DoS) Attack
Attacker
Init Comm.: PLC IP+Port 102
Challenge question
Challenge response
Challenge response
Session OK
Crafted TCP Packets
Network
PLC
Challenge question
Session OK
Init Comm.: PLC IP+ port 102
Crafted TCP Packets

## Slide 9: Attack Demonstration
Attack Setup
Phase 1: Man-in-the-Middle Attack
Engineering Workstation
Rockwell PLC
Internet

## Slide 10: Attack Demonstration
Result
  Recoverable major fault on the PLC
  Stopping the running process
  Unavailability of PLC for further online requests
  Caused DoS attack
Resolution
  Manual restarting of the PLC through a power cycle
  Clear major fault
Phase 2: DoS Attack

## Slide 11: ABAC Gateway

## Slide 12: Test Bed
NGAC-ABAC Implementation on Raspberry Pi3
  Python Vakt library
  Example Policy
Engineering Workstation
ABAC Gateway
Raspberry Pi3
Rockwell PLC
Wi-Fi
LAN

## Slide 13: Test Bed
Crafted TCP Packet
  Device ID of Engineering Workstation: ‘velpi’
  Allowed device ID for establishing the communication with Compact Logix: ‘Equip21LOrgABC’
Communication Request Packet

## Slide 14: Test Bed
Policy Verification for ‘Register Session’ Request
DoS attack prevented based on invalid device ID

## Slide 15: Verification: PLC Operates without ABAC Gateway
CPN Block Diagram
Three CPNs:
  User, Network, and PLC
User sends a request packet to initialize communication with PLC
The PLC receives the request and replies with a challenge question
The user sends the challenge response, and the PLC confirms that the session is OK to be established.
The user sends a command to PLC to be executed and receives a response with PLC status

## Slide 16: Verification: PLC Operates without ABAC Gateway
CPN Demo: TCP Packets traveling between User and PLC through Network

## Slide 17: Verification: PLC Operates without ABAC Gateway
Testcases: CPN Tokens demonstrate legal access (first 3 tokens) and attacks (last 2 tokens)
TC#4: ATTACKER-1 impersonates USER and obtained the same access discretion, but DAC blocked its TCP request packet. (Testcase failed)
TC#5: ATTACKER-2 impersonates ADMIN, gained its discretion, and stopped the PLC. (Testcase passed)

## Slide 18: Verification: PLC Operates with ABAC Gateway
CPN Block Diagram: Four CPNs (User, Network, ABAC Gateway, and PLC)
ABAC Gateway: contains three sub CPN blocks: Authentication Module, Comm. Handler, and Access Control Module (NGAC)
Any TCP Packet sent from User to PLC must go through the ABAC Gateway

## Slide 19: Verification: PLC Operates with ABAC Gateway
CPN Demo: TCP Packets traveling between User and PLC through Network and ABAC Gateway

## Slide 20: Verification: PLC Operates with ABAC Gateway
Testcases: CPN Tokens demonstrate legal access (first 3 tokens) and attacks (last 3 tokens)
TC#6: ATTACKER-2 impersonates ADMIN, sends setup command, but it is denied by the ABAC Gateway. (Testcase failed)

## Slide 21: Formal Analysis
State-Space Analysis for Use Case 2
State-Space Analysis for Use Case 1
The authentication property: verifying the identity of a user, process, or device
The authorization property: verify that a requested action or service is granted for a specific resource
In DAC access control mechanism, the is no guarantee that the attacker cannot impersonate an administrator user with the full privilege
The ABAC gateway verifies the access based on NGAC policy comprising user attributes, environment, resource, and operation attributes

## Slide 22: Conclusion
  It may be impossible to patch all the vulnerabilities of ICS.
  The solution is to protect against authentication vulnerabilities in PLC
  We developed NIST NGAC Attribute-Based Access Control for PLC protection.
  We built a testbed to demonstrate the ABAC Gateway
  Formal Verification is executed to verify the PLC system in Use Cases
    PLC operates without ABAC Gateway
    PLC operates with ABAC Gateway
  Result shows ABAC Gateway effectively hardens the PLC security

## Slide 23: Future Work
  Currently, we are investigating the use of NIST NGAC for the security hardening of other devices in an ICS environment.
  Next, we will analyze the latency, performance, and throughput of the ICS due to the incorporation of the ABAC module

## Slide 24: Acknowledgement
  NSF
  NIST
  Cyber Risk Research
  Statnett
  AMI
  ARL
  New Push

## Slide 25: Questions?
Thank you!